## Slide 1: Chapter 14: Quality Attribute Modeling and Analysis

## Slide 2: Outline
Modeling Architectures to Enable Quality Attribute Analysis
Quality Attribute Checklists
Thought Experiments and Back-of-the-Envelope Analysis
Experiments, Simulations, and Prototypes
Analysis at Different Stages of the Life Cycle

## Slide 3: Modeling Architectures to Enable Quality Attribute Analysis
Some quality attributes, most notably performance and availability, have well-understood, time-tested analytic models that can be used to assist in an analysis.
By analytic model, we mean one that supports quantitative analysis. Let us first consider performance.

## Slide 4: Performance Models
Parameters: arrival rate of events, chosen queuing discipline, chosen scheduling algorithm, service time for events, network topology, network bandwidth, routing algorithm chosen
arrivals
queue
server
results
Scheduling algorithm
Routing of messages

## Slide 5: Allocation Model for MVC

## Slide 6: Queuing Model for MVC
Arrivals
View sends requests to Controller
Actions returned to View
View
Users Generate Requests
Controller
Model
1
3
2
4
5
Actions returned to model
Model sends actions to View

## Slide 7: Parameters
To solve a queuing model for MVC performance, the following parameters must be known or estimated:
  The frequency of arrivals from outside the system
  The queuing discipline used at the view queue
  The time to process a message within the view
  The number and size of messages that the view sends to the controller
  The bandwidth of the network that connects the view and the controller
  The queuing discipline used by the controller
  The time to process a message within the controller
  The number and size of messages that the controller sends back to the view
  The bandwidth of the network from the controller to the view
  The number and size of messages that the controller sends to the model
  The queuing discipline used by the model
  The time to process a message within the model
  The number and size of messages the model sends to the view
  The bandwidth of the network connecting the model and the view

## Slide 8: Cost/benefit of Performance Modeling
Cost: determining the parameters previously mentioned
Benefit: estimate of the latency
The more accurately the parameters can be estimated, the better the predication of latency.
This is worthwhile when latency is important and questionable.
This is not worthwhile when it is obvious there is sufficient capacity to satisfy the demand.

## Slide 9: Availability Modeling
Another quality attribute with a well-understood analytic framework is availability.
Modeling an architecture for availability—or to put it more carefully, modeling an architecture to determine the availability of a system based on that architecture—is a matter of determining the failure rates and the recovery times of the components.
Just as for performance, to model an architecture for availability, we need an architecture to analyze.
Suppose we want to increase the availability of a system that uses the Broker pattern, by applying redundancy tactics.

## Slide 10: Availability Modeling
Three different tactics for increasing the availability of the broker are:
  active redundancy (hot spare)
  passive redundancy (warm spare)
  spare (cold spare).

## Slide 11: Making Broker More Available
Key:
process:
message:

## Slide 12: Applying Probabilities to Tactics
Using probabilities to model different tactics
  When two events A and B are independent, the probability that A or B will occur is the sum of the probability of each event: P(A or B) = P(A)+ P(B).
  When two events A and B are independent, the probability of both occurring is P(A and B) = P(A) • P(B).
  When two events A and B are dependent, the probability of both occurring is P(A and B) = P(A) • P(B|A), where the last term means “the probability of B occurring, given that A occurs.”

## Slide 13: Passive Redundancy
Assume
  failure of a component (primary or backup) is independent of the failure of its counterpart
  assume failure probability of both is the same: P(F)
Then probability that both will fail is: 1 - P(F)2
Can also estimate probability of failure given other tactics.
Then given a cost of implementing appropriate tactic we can do cost/benefit analysis

## Slide 14: Calculated Availability for an Availability-Enhanced Broker

## Slide 15: Maturity of Quality Attribute Models
Quality Attribute | Intellectual Basis | Maturity / Gaps
Availability | Markov models; Statistical models | Moderate maturity in the hardware reliability domain, less mature in the software domain. Requires models that speak to state recovery and for which failure percentages can be attributed to software.
Interoperability | Conceptual framework | Low maturity; models require substantial human interpretation and input.
Modifiability | Coupling and cohesion metrics; Cost models | Substantial research in academia; still requires more empirical support in real-world environments.
Performance | Queuing theory; Real time scheduling theory | High maturity; requires considerable education and training to use properly.
Security | No architectural models | 
Testability | Component Interaction Metrics | Low maturity; little empirical validation.
Usability | No architectural models | 

## Slide 16: Quality Attribute Checklists
A quality attribute checklist provides a means of:
  Checking requirements. Do the requirements capture all of the nuances of a particular quality attribute?
  Auditing. Does the design satisfy all of the aspects necessary for a certification process.

## Slide 17: Security Checklists
Security checklists are common.
  Vendors who accept credit cards should conform to the PCI (Personal Credit Information) standard
  Electricity producers have security checklists to prevent attacks on critical infrastructure
Checklists have both:
  Product requirements. E.g. the PCI checklist states that the security code on the back of the credit card should never be stored.
  Process requirements. E.g. patches should be applied promptly and there should be someone who has the organizational responsibility to ensure that they are.

## Slide 18: Thought Experiments
A thought experiment is mentally or verbally working through a particular scenario.
  Commonly done by the architect during design to explore alternatives.
  Also done during evaluation/documentation to convince third parties of the wisdom of particular design choices

## Slide 19: Thought Experiment Steps
Enumerate the steps of a use case
At each step, ask {yourself, the architect}
  What mechanism is being implemented to support the achievement of which particular quality requirement?
  Does this mechanism hinder the achievement of other quality attribute requirements?
Record problems for later deeper analysis or prototype building

## Slide 20: Back-of-the-Envelope Analysis
Analysis does not need to be precise or detailed.
Rough analysis serves for many purposes. E.g. “the volume of traffic generated by this source should be well within the bounds handled by modern infrastructure”
Only do deeper analysis for questionable areas or important requirements.

## Slide 21: Experiments, Simulations, and Prototypes
Many tools can help perform experiments to determine behavior of a design
  Request generators can create synthetic loads to test scalability
  Monitors can perform non-intrusive resource usage detection.
These depend on having a partial or prototype implementation.
  Prototype alternatives for the most important decisions
  If possible, implement prototype in a fashion so that some of it can be re-used.
  Fault injection tools can induce faults to determine response of system under failure conditions.

## Slide 22: Simulations
Event based simulators exist that can be used to simulate behavior of system under various loads
  Must create the simulation.
  Must have a variety of different loads and responses to check for.

## Slide 23: Analysis During Requirements and Design
Different types of analysis are done at different stages of the life cycle
Requirements:
  Analytic models/back of the envelope analysis can help capacity planning
  Checklists can help ensure capture correct set of requirements
Design:
  Prototypes can help explore design options
  Analytic models or simulation can help understand potential bottlenecks
  Checklists can help determine if used a correct mechanism

## Slide 24: Analysis During Implementation or Fielding
Experiments and synthetic load tests can be used during the implementation process or after fielding
Monitors can be used after fielding to determine actual behavior and find bottlenecks.

## Slide 25: Analysis at Different Stages of the Lifecycle
Life-Cycle Stage | Form of Analysis | Cost | Confidence
Requirements | Experience-based analogy | Low | Low-High
Requirements | Back-of-the-envelope | Low | Low-Medium
Architecture | Thought experiment | Low | Low-Medium
Architecture | Checklist | Low | Medium
Architecture | Analytic Model | Low-Medium | Medium
Architecture | Simulation | Medium | Medium
Architecture | Prototype | Medium | Medium-High
Implementation | Experiment | Medium-High | Medium-High
Fielded System | Instrumentation | Medium-High | High

## Slide 26: Summary
Analysis is always a cost/benefit activity
  Cost is measure of creating and executing the analysis models and tools
  Benefit depends on
    Accuracy of analysis
    Importance of what is being analyzed
Analysis can be done through
  Models for some attributes
  Measurement
  Thought experiments
  Simulations
  Prototypes