## Slide 1: SurePark System
1st Decomposition

## Slide 2: Physical View
SurePark Manager-A
Facility Controller #1
SurePark DB
Legend
Arduino Hardware
Client Machine
Server Machine
Process
Database
Network Connection
Garage Boundary
…
Facility Controller
#n
…
Web Service
Web Browser
Web Browser
Read/Write
Read Only

## Slide 3: Physical View (Demo System)
SurePark Manager-A
Facility Controller #1
SurePark DB
Legend
Arduino Hardware
Client Machine
Server Machine
Process
Database
Network Connection
Localhost Connection
…
Web Service
Web Browser
Web Browser

## Slide 4: Dynamic View
Web Browser
SurePark Manager-A
Facility Controller
Web Service
SurePark DB
Legend
Process
Database
HTTP
TCP/IP
BSON
Read Only
Read/Write

## Slide 5: Entity Catalog
Entity | Desctiption
Web Browser | Users, attendants and owner can access their own UI through the web browser provided by the web server.
Web Service | Provides users with the functions of sign-up, log in, reservation, monitoring facilities and/or showing parking statistics based on data retrieved from SurePark DB. Sends information to SurePark Manager for DB updates.
Facility Controller | Controls parking facilities; get the status of parking slots, turn on/off LEDs, detect a car at the gates and open/close the gates. Receives data from SurePark Manager to control LEDs and/or gates. Sends data to SurePark Manager to update the status of parking slots.
SurePark Manager | Handles show-up and no-show scenarios based on DB information. Updates SurePark DB when a user has signed up, a reservation has been made or facility status has been changed.
SurePark DB | Keeps all of the data about users, garages and reservations. Only can be updated by SurePark Manager.

## Slide 6: Rationale
SurePark Manager-A
Facility Controller #1
SurePark DB
…
Facility Controller #n
…
Web Service
Web Browser
Web Browser
Client-Server Pattern
Client-Server pattern promotes modifiability and reuse, by factoring out common services and modifying them in a single location. Also, it improves scalability and availability by centralizing the control of resources and services.
Repository Pattern
This pattern supports modifiability by decoupling producers and consumers of data.

## Slide 7: Rationale (Cont’d)
Modifiability is one of the most important QAs of the SurePark system. An engineer needs to scale up the system within a week. We have divided the whole system into 5 parts according to their responsibilities, and applied client-server and repository pattern to connect each parts.

## Slide 8: Static View
Facility Controller Application
SurePark Manager Application
Web Service Application
Shares common protocol
Shares common DB schema using JSON
Legend
Package
Note

## Slide 9: Rationale (Cont’d)
Client-Server Pattern
  Pros: scale, in that it is easy to add more clients and easy to add more data
  Cons: reliability, performance, security, complexity, modifiability (can be hard to change data structure, protocols, or identify of servers)
Repository Pattern
  provides a structure to store and provide access to all of the data about users, garages and reservations

## Slide 10
SurePark Manager – Static View
Common
Management Service
Control Service
Shares
FC-SM protocol
Shares common DB schema
&
Shares SM-WS protocol
Legend
Facility Controller
Web
Service
SurePark Manager Boundary
Package
Note
Uses

## Slide 11
SurePark Manager – Dynamic View
Web Service
Facility Controller
Legend
Process
SurePark Manager Process
Object
Control Service
Management
Service
SurePark DB
TCP/IP Packet data flow
DB control flow
Read/Write
Read
Call-Return