## Slide 1: Sure-Park System Final Presentation
Team 3(Infinite Challenge)
Namjin Lee(Team Leader) Jack Oh, Charles Park, Joan Kim, Jaeheon Kim

## Slide 2: Contents
1. Introduction
2. Architectural Drivers
3. System Context
4. Architectural Design
5. Protocol
6. Test
7. Time Log
8. Artifacts
9. Lesson Learned
Q&A
APPENDIX

## Slide 3: 1. Introduction
We are an LG team and we were assigned this project 7 weeks ago. There are 5 team members and a mentor who have set out to build a new parking garage management system called “Sure Park”.
Role | Assign | Responsibility
Mentor | Mel Rosso-Llopart | Coaching team members
Team leader | Namjin Lee | Check time log and risk management
Architect | Jaeheon Kim | Design system architecture Developed “Sure Park Manager” part.
Integration | Jack Oh | Integrate all artifacts(source code, documents …etc). Developed “Web Service” part.
Test | Charles Park | Test and delivery. Developed “Facility Controller” part.
Documentation | Joan Kim | Create document artifacts. Developed “Sure Park Manager” part.

## Slide 4: 2.1 Functional Requirement (1)
ID | Functional Requirement | Description
FR01 | The system must detect cars in parking space. | Arduino H/W control
FR02 | The system must open and close the entry/exit gates. | 
FR03 | The system must change the entry/exit LED color and turn on/off stall LEDs. | 
FR04 | The system must detect presence of a car when cars arrive at the entry/exit gates. | 
FR05 | The system shall allow drivers to reserve parking spaces. Reservations will be made via a mobile app, a laptop, or a desktop app for drivers. | Reservation system for drivers
FR06 | For reservation, drivers must sign up the system so that the system can prevent from unauthorized users. | 
FR07 | The system must provide available number of parking slots to drivers. | 
FR08 | Drivers must provide the day and time they would like to park, and credit card information (payment information) after logging in system. | 
FR09 | The system must return a confirmation information to the driver if reservation is succeed. | 
FR10 | The system must check the confirmation information to verify the deriver's information and reservation. | When drivers come up an entry gate

## Slide 5
2.1 Functional Requirement (2)
ID | Functional Requirement | Description
FR11 | “Grace period” must be configurable. | No-show process
FR12 | If the driver does not show up at the start of their reservation time, the system must operate the "grace period". | 
FR13 | If the driver doesn't show up within the grace period, the system must cancel the reservation. | 
FR14 | The system must calculate the total parking fee by hour and it shall charge on their credit card. | Charge system
FR15 | The system must show which parking spots are occupied and which are opened. | Monitoring system for attendants
FR16 | The system must show how long the car has occupied the particular parking space. | 
FR17 | The system must show the status when a driver parks in the wrong parking space and must automatically reassign parking spaces and correlate associated reservations. | 
FR18 | The system must show the facility usage and revenue. The facility usage must include average occupancy, peak usage hours, parking slot statistics. | Management system for owner
FR19 | The system shall extend analysis algorithms or applications without disrupting operations. | Management system for owner Extend system
FR20 | The system must provide login system for preventing unauthorized users. | System security
FR21 | The system must not allow anyone to view facility data (reservations, credit cards, etc.) except owner. | 

## Slide 6
2.2 Quality Attribute Utility
ID | Quality Attribute | Description | Difficulty(D) | Priority (P) | Total Score (D x P)
QA01 | Scalability | Scale out to other parking facilities | 3 | 3 | 9
QA02 | Availability | Detect malfunction of the Sure park system’s software | 9 | 9 | 81
QA03 | Security | Protect data and information from unauthorized access | 3 | 9 | 27
QA04 | Extensibility | Add more analysis algorithms or analysis applications | 3 | 3 | 9
QA05 | Performance | Retrieve an available parking slot ASAP. | 1 | 3 | 3
QA06 | Usability | Obtain basic statistics on facility usage. | 1 | 9 | 9
QA07 | Interoperability | Communicate between facility controller and Sure Park system. | 3 | 3 | 9
QA08 | Modifiability | Scale up/out to parking facilities | 9 | 9 | 81
※ Greater number equals to higher priority

## Slide 7
2.3 Business Constraint
ID | Business Constraint | Description
BC01 | Reducing complain | GTPS wants to reduce driver frustration when customers find available parking slots and reserve them.
BC02 | Increasing profits | More efficient space utilization is needed.
BC03 | Reducing liabilities | It is needed to reduce traffic congestion and the chance for accidents inside the parking facilities.
BC04 | Reducing operating costs | It is required to utilize personnel efficiently and reduce the number of employee.
BC05 | Applying other garage | GTPS would like to market the system to other garage owners around the world.
BC06 | Delivery | The system should be delivered in 5 weeks.
BC07 | Availability of workforce | The team is consists of 5 members. Java expert is only 1 person.
BC08 | Access the garage | Only a car can get in/out the garage.
BC09 | Parking | A driver who made a reservation can park a car.
BC10 | Charge | The system will charge a check by 30 minutes.
BC11 | Reservation | A driver can make a reservation within 3 hours.
※ More constraints added after meeting with Tony (BC07~BC11)

## Slide 8
2.4 Technical Constraint
ID | Technical Constraint | Description
TC01 | H/W System | Wi-Fi enabled Arduino(mega 2560) - Flash Memory: 256KB of which 8KB used by bootloader - SRAM: 8KB - EEPROM: 4KB - Clock Speed: 16MHz
TC02 | Programming language | For development Arduino: C/C++ For server and application: Java
TC03 | Network | Wi-Fi Wi-Fi configuration
TC04 | Facility parts | Add more sensors, alarm LEDs, and gate servos of the same type to the existing controller. A controller can have maximum 10 slots.
※ More constraints added after meeting with Tony (TC04)

## Slide 9: 3. System Context
The scope of SurePark system is shown below.
Drivers can reserve a parking space by using a laptop or a phone.
Parking attendants can monitor parking facilities.
For the owner, the system provides facility usage statistics including average occupancy, peak usage hours, parking slot statistics, and revenue.
The system controls entry/exit gates and LED indicators based on the status of sensors.

## Slide 10
4.1 1st Decomposition (1)
Physical View

## Slide 11
4.1 1st Decomposition (2)
Dynamic View

## Slide 12
4.1 1st Decomposition (3)
Static View

## Slide 13
Entity | Description
Web Browser | Users, attendants and owner can access their own UI through the web browser provided by the web server.
Web Service | Provides users with the functions of sign-up, log in, reservation, monitoring facilities and/or showing parking statistics based on data retrieved from SurePark DB. Sends information to SurePark Manager for DB updates.
Facility Controller | Controls parking facilities; get the status of parking slots, turn on/off LEDs, detect a car at the gates and open/close the gates. Receives data from SurePark Manager to control LEDs and/or gates. Sends data to SurePark Manager to update the status of parking slots.
SurePark Manager | Handles show-up and no-show scenarios based on DB information. Updates SurePark DB when a user has signed up, a reservation has been made or facility status has been changed.
SurePark DB | Keeps all of the data about users, garages and reservations. Only can be updated by SurePark Manager.
4.1 1st Decomposition (4)
Entity Catalog

## Slide 14
4.1 1st Decomposition (5)
Rationale
To achieve modifiability, we have divided the whole system into 5 parts based on their responsibilities, and applied client-server and repository pattern to connect each parts.
QA Scenario of Modifiability (QA08)
The developers want to design scale up/out the system. The new system is implemented and tested in a week.

## Slide 15
4.2 2nd Decomposition: SurePark Manager
Network communication can be failed because of the many reasons.
Tactics for detecting fault: Heartbeat or Ping/Echo
To reduce network traffic, we select Heartbeat.
Rationale
QA Scenario of Availability (QA02)
Sure park system’s software detects software failure. In this case, Sure Park system’s software notify attendants in 30 seconds and restart in 1mins.

## Slide 16
4.3 2nd Decomposition: Web Server (1)
Secure applications should not allow users to get through a back door that allows them to view or edit sensitive data. Single Access Point helps solve this problem by limiting application entry to one single point.
Rationale
QA Scenario of Security (QA03)
Users log in the system and get the permission to access the authorized data and information. The unauthorized user tries to access the data and information which are permitted only attendants and owner. The system prevents all unauthorized access.

## Slide 17
4.3 2nd Decomposition: Web Server (2)
Groups of users will have different roles that define what they can and can not do.
Sure Park system provides different Roles to each user; creating, maintaining and viewing the data.
Rationale

## Slide 18
5. Protocol
Start Symbol | Facility Id | Code | Value | End Symbol
1byte($) | 4byte | 1byte | Variable length | 1byte(\n)
SurePark Manager to Facility Controller
Code List:
I = Information, S = Slot Status, E = Entry Gate, X = Exit Gate, L = LED.
Packet Example
Slot status packet: $1001S1001\n (Slot 0 and 3 are occupied.)
Heartbeat packet: $1001\n (Only have facility Id.)
SurePark Manager to Web Service
Client-server communication with JSON
Reference: http://www.json.org/

## Slide 19
ID | Functional Requirement
FR05 | The system shall allow drivers to reserve parking spaces. Reservations will be made via a mobile app, a laptop, or a desktop app for drivers.
FR06 | For reservation, drivers must sign up the system so that the system can prevent from unauthorized users.
FR07 | The system must provide available number of parking slots to drivers.
FR08 | Drivers must provide the day and time they would like to park, and credit card information (payment information) after logging in system.
FR09 | The system must return a confirmation information to the driver if reservation is succeed.
6. Test
ID: UC01 | Description
Title | (FR05 ~ FR09) Reserve parking spaces
Stakeholders | A driver who would like to reserve a parking space.
Preconditions | The driver must satisfy with FR06,FR20
Main success scenario | 1) The Sure-Park system allows an authorized driver to reserve a parking slot (FR05). 2) The system shows available number of parking slots to the driver (FR07). 3) If a parking slot is available, the driver needs to input the day and time they would like to park, and credit card information (FR08). 4) If all information is ok, the system provides confirmation information to drivers (FR09).
Post conditions | The reservation was confirmed.
Alternate scenario | ….
Use Case
Test
Case

## Slide 20
7. Time Log
Chart: 
| Design | Documentation | Implement | Integration Test | Management | Meeting
총합계 | 2.458 | 1.6679 | 3.3673 | 1.3053 | 0.091667 | 2.9389
Chart: 
| 42513 | 42514 | 42515 | 42516 | 42517 | 42518 | 42519 | 42520 | 42521 | 42522 | 42523 | 42524 | 42525 | 42526 | 42527 | 42528 | 42529 | 42530 | 42531 | 42532 | 42533 | 42534 | 42535 | 42536 | 42537 | 42538 | 42539 | 42540 | 42541 | 42542 | 42543 | 42544
Actual | 0 | 0.30972 | 0.62223 | 0.9299 | 0.9299 | 0.9299 | 0.9299 | 0.9299 | 1.1098 | 1.3386 | 1.6133 | 1.9095 | 1.9512 | 2.4754 | 3.0838 | 3.9154 | 4.275 | 4.4447 | 4.4447 | 4.738 | 5.1866 | 5.8663 | 6.0514 | 6.9437 | 6.9437 | 7.1241 | 7.9384 | 9.0853 | 10.2963 | 11.7963 | 13.2962 | 14.5072
Planed | 0.52083 | 1.0417 | 1.5625 | 2.0833 | 2.6042 | 2.6042 | 2.6042 | 2.6042 | 3.125 | 3.6458 | 4.1667 | 4.6875 | 4.6875 | 4.6875 | 5.2083 | 5.7292 | 6.25 | 6.7708 | 7.2917 | 7.2917 | 7.2917 | 7.8125 | 8.3333 | 8.8542 | 9.375 | 9.8958 | 9.8958 | 9.8958 | 10.4167 | 10.9375 | 11.4583 | 11.9792
GAP
Why gap happened?
This chart looks like a pregnant lady chart but the gap happened the first week.
We had a trouble adjusting to the time difference in the first week.
We had a burden of reading assignment as we expected.

## Slide 21
8. Artifacts
No. | File Name | Discription
1 | SurePark_Initial_TEAM3.pptx | Initial presentation document
2 | SurePark_Final_Presentation_TEAM3.pptx | Final presentation document
3 | SurePark_ADS_TEAM3.docx | Architectural Driver Specification document
4 | SurePark_ADD_TEAM3.docx | Architectural Design Document
5 | SurePark_TestCase_TEAM3.xlsx | Test case document
6 | SurePark_TimeLog_TEAM3.pdf | Time log
7 | SurePark_GanttChart_TEAM3.xlsx | Gantt chart
Document
Source Code
No. | Application | Language | LOC
1 | Facility Controller | C | 616
2 | SurePark Manager | JAVA | 1263
3 | Web Service | HTML5 CSS JAVA SCRIPT | 1650

## Slide 22
9. Lesson Learned
Using COTS is not free
MongDB, Google Chart and Java script libraries.
Google Chart cannot be used in the demonstration because the router is not connected to the internet.
Some of Java script libraries caused network problems and it takes some time to find the root causes and fix them.
Development Tools
Toggl: a time tracking application to record our time log. It makes easier for us to manage time.
Smartsheet: Gantt chart
GitHub: configuration management tool
Perspective
Before CMU: Use only static view or mixed perspective.
After CMU: We can distinguish three perspectives.
Interface
Once the interface has been fixed, it becomes a constraint.
We have experienced this kind of situation and had to spend our resources because of changing some protocols.

## Slide 23
Q & A

## Slide 24
APPENDIX
All UIs are designed to show their contents within 1 step.
Rationale
QA Scenario of Usability (QA06)
The owner wants to check basic statistics on facility usages. The owner can show statistic report in 3 step after login.